# Introduction
The purpose of the Lock Controller is to manage the E6000 front lock by:
- Measuring the position of the lock (in terms of needle or pusher count),
- Controlling the solenoid drivers, and
- Responding to and sending messages to and from the PC.
In addition, there are interfaces to control E3000A and 4600 motors.
# Copyright Statement
A copyright statement is attached to every file and product created by the SoftKnit21 project. It takes the form of the copyright statement for this document:
This document describes the Lock Controller hardware for attachment to a Passap E6000 knitting machine.
Copyright (C) 2020 Owen Mace and Odile Lambert.
This document is free information: you can redistribute it and/or modify it under the terms of the GNU General Public License as published by the Free Software Foundation, either version 3 of the License, or (at your option) any later version.
This program is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for more details.
You should have received a copy of the GNU General Public License along with this program. If not, see <https://www.gnu.org/licenses/>.

# Components
The components of the Lock Controller hardware are:
- An Arduino Nano microcomputer consisting of:
  - A 4 inch x 4 inch (approximately) Printed Circuit Board (PCB), and
  - Container that attaches to the E6000 rear rail of the stand,
- A 15 volt DC, 1 amp (approximately) power pack and main cable, and
- Cables connecting the PC with the Lock Controller.
Descriptions of these Components follow.
## Microcomputer Component
The microcomputer section consists of a PCB with the following electronic components:
- An Arduino Nano microcomputer with a USB port for communication with the PC,
- Passive components used to connect with the E6000 Front Lock via a 6 pin circular DIN socket,
- Sockets to connect to E3000A and 4600 motor controllers,
- An LED which can be programmed for any diagnostic purpose, and
- A 3 mm jack socket to connect the +15 volt power supply, a fuse and an LED to indicate the presence of the +15V supply.
Each of the two signals from the Front Lock (CRef and CSense) have a 2.2 kΩ pullup resistor and a 10 nF capacitor to eliminate multiple transitions of the signals. Each of the two signals to the Front Lock (LTR and RTL) have a series 2.2 kΩ current limiting resistor. All four digital connections to the Front Lock are protected by 4.7 volt zener dodes in the same manner as the Console.
Both the +15 volt and +5 supplies have large capacitors to reduce voltage fluctuations and voltage dividers connected to analogue inputs of the Arduino Nano so that those voltages can be monitored.
Interfaces for the motors are:
- An RJ45 socket for a connection to an Electra 4600 motor, and
- A pair of audio jacks for connection to an E3000A motor. Since the E3000A controller consists of 50 VDC relay logic, the Arduino is isolated from the E3000 by reed relays.
The specified relays are COTO 9007-05 reed relays. The 9007-05-01 version (preferred) has a protection diode connected across the coil and thus an external protection diode is not required. Nevertheless, provision for protection diodes has been made in the circuit.

An image of the PCB approximately full size (in the printed version of this document) was taken on 4 May 2020:
Along the top of the PCB, from the left are:
- An orange indicator LED,
- Arduino Nano with a miniature USB socket for a cable to the PC,
- 6 pin DIN socket for the Spiral Cable to the Front Lock,
- Barrel Jack for +15V supply, and
- LED indicating the presence of +15V.
Along the left Side from the top are:
- RJ45 socket for 4600 motor, and
- two Audio sockets for E3000A.
A 1 A slow blow fuse, as in the Console, is on the right.
Two reed relays are in the lower left. In this case they are COTO 9007-05-01 and so diodes are not required; D8 and D10 are strapped.
Connections to the RJ45 (R13 to R16 below the Arduino Nano) are not installed.
The passive components to the right of the Arduino Nano are associated with the interface to the Front Lock.
The empty space to the right of the relays is for a Bluetooth® module.
## Container Component
A container with adequate ventilation holds the PCB and attaches to the upper rail of the E6000 stand in a manner similar to the yarn masts. Motor connections are provided on the left side of the container for convenience.
## Power Pack Component
The Power Pack supplies +15volts to the Front Lock. Measurements have shown that the Front lock consumes about 180 mA at +15 V but there are large (1 amp) and short pulses (less than 1 msec) when pushers are operated. Experiments have shown that the Power Pack must be capable of supplying that current while limiting current transients of less than around 200 mV. A Power Pack with a 1 to 3 amp capability seems to be satisfactory. A 12 volt power pack with similar specifications has also been used successfully.
If an Electra 4600 motor is connected to the Lock Controller, the current drain rises to over 500 mA.
## Cable Component
The Cable Component consists of:
- A USB Cable Component connects the mini-USB socket on the Arduino Nano with a conventional USB-B on the PC and is used to program the Arduino and convey messages between the PC and Lock Controller Arduino Nano. While a short USB cable is often supplied with the Arduino Nano, a suitable extension is required to connect from the LC to the PC,
- A power cable is normally part of the +15V power pack,
- Cable for connection to motors:
  - An ethernet cable with RJ45 connectors for connection to an Electra 4600 motor, or
  - Two audio cables with 3 mm audio jacks on each end for connection to an E3000A motor.
## Mounting
The container is designed to be mounted on the rear rail of the E6000 stand. A convenient location is at the motor/colour changer end of the stand, as illustrated below. All cables, except the Electra 4600 cable, are in place. The hole visible in the centre of the printed circuit board allows entry of a Phillips head screw driver to tighten the screw holding the container in place: