## Repairing a Console
Recently I received a Console with no serial number – my first Console repair task. It looked like an old model with original “03” chips and a UK plug, which was quickly replaced.
A multimeter showed that the +5V supply was OK but the fuse on the +15V supply (for buzzer, card reader and front lock) had blown, despite the Console printed circuit board (PCB) drawing a DC current around 50 mA. This is a common problem. My suspicion was that the 30+ year old capacitors in the +15V power supply were faulty and blowing the fuse at turn-on. Replacement of two electrolytic capacitors, C2 (details below) and C5 as well as the bridge rectifier (D2) and slow blow 1A fuse fixed the supply problem. (That is an insulated screw driver to the right of the transformer.)

However, the buzzer was still not working and so I followed the PCB trace from the regulator (REG2) to the LM339 comparator (IC9, pin3) and discovered a break, probably at a via. Bypassing the break with a wire restored the buzzer but the “MEMO” message continued to appear when the Console was turned on. Once again a broken trace but this time a tiny nick in the trace between D10 and D13 near D13 had open circuited the trace. Again, a wire bypassing the break brought life to the memory and no more “MEMO” messages. Inspecting other Console PCBs showed that this was a one-off fault and not a fault with the PCB artwork.
To check all was well, I left the console on for seven hours and tested that it operates pushers as expected. All OK so now it can be returned to its owner.
The final problem was the back of the Console. The holes where screws attach the back to the front were broken, so there was only one screw able to hold them together. I carefully ground down the remains of the holes and then cut some 3 mm polycarbonate sheet into narrow strips. Then I used super strength epoxy to glue the polycarbonate pieces over the holes and left it for 72 hours to gain maximum strength. Reassembly after drilling hole for the screws and all seems well.
## Instructions for Repairing the +15V Supply
Diagnosis: Buzzer does not sound when keys are pressed, card reader does not work and front lock does not operate pushers.
Skills: familiarity with electronics and PCBs. Ability to solder PCBs.
Tools: Phillips head screw driver preferably magnetised, electronics soldering iron, solder sucker, small pliers and side cutter suitable for electronic work.
Parts: Capacitors C2 (2200µF, 50V) and C5 (220µF, 25V)and bridge rectifier (D2 1A, 100+V), 1A slow blow fuses (SI1). Potentially the regulator 7815 (REG2).
Disassembly: Unscrew the four bolts joining the from and back halves of the case together. Unscrew all the phillips head screws securing the PCB to the front case and loosen the screw retaining the mains cable. Remove the four longer screws securing the transformer. Carefully lift out the PCB, then unscrew the two bolts holding the two regulators (REG2 and REG3) to the heat sink. Turn the board over and unscrew the two screws holding the heat sink in place, then remove the heatsink and plastic stands. Unsolder the capacitors and bridge rectifier and replace them and the fuse. Check that +15V appears on pin 3 of LM339 (IC9). Reassembly is the reverse of disassembly.
Test: Check that the buzzer sounds and the front lock operates the pushers correctly. Check the card reader, if used by the owner. Leave on for hours and check voltages.
## Acknowledgement
Thanks to Richard Croucher for his immense help directing me towards likely faults.